## Slide 1: Power Containers: An OS Facility for Fine-Grained Power and Energy Management on Multicore Servers
Kai Shen, Arrvindh Shriraman, Sandhya Dwarkadas,
Xiao Zhang, and Zhuan Chen
University of Rochester
Shriraman is now at Simon Fraser University; Zhang is now at Google.

## Slide 2: Problem Overview
Power/energy are important for data centers and servers
Dynamic power usage on modern hardware
  Power proportionality: 5% idle power on Intel SandyBridge
  Workload dependency: 3:2 power ratio on same machine
A server runs many requests from users
  Request is basic unit of user-initiated work
    Carbon footprint of a web click?
    Power viruses in cloud
  Request is basic unit of load distribution
   Motivations for per-request power accounting and control

## Slide 3: Power Containers on Multicore Servers
Challenges:
  Concurrenct, fine-grained request activities over multiple stages
  Complex multicore power sharing; insufficient direct measurement
Approach:
  Event-based power modeling + request tracking
Contributions on power modeling:
  Account for multicore shared power
  Use online measurement to mitigate power model inaccuracy
Contributions on request tracking:
  Online request tracking and control
  OS support transparent to applications

## Slide 4: Multicore Power Attribution to Concurrent Tasks
Bellosa’s event-based power model
  Assumes direct relationship between one’s physical activities (instructions, cache references, bus activities, …) and power
On a multicore, maintenance of shared resources consumes power when at least one core is active
  Such shared power is not affected by one’s own physical activities, but rather depends on the level of multicore sharing
  Our approach: evenly attribute to concurrently running requests
  Implemented efficiently by local estimation of multicore sharing level (to avoid expensive global coordination and cross-core interrupts)

## Slide 5: Measurement-Assisted Online Model Correction
Classic event-based power modeling is being questioned
  [McCulough et al. 2011] shows pessimistic results
  We find large model errors due to different characteristics between production and calibration workloads (worst for unusual workloads)
Our approach
  Online power measurement can help re-calibrate power model
  Measurement has delays, needs alignment with modeled power

## Slide 6: Request Power Accounting
Request context tracking in a multi-stage server
  Past techniques either require offline analysis, or at application level
Our approach
  Track request propagation events (sockets, forks, …) at the OS
  Attribute and control power at proper request context
  Imperfect now: miss 1/3 of power in GoogleAppEngine

## Slide 7: Online Overhead
Overhead depends on frequency of periodic activities; low overhead (<1%) for sufficiently frequent activities
Periodic maintenance of power containers
  Reading hardware counters, power modeling, updating request stats  2948 cycles, 1656 instructions, 16 floating point ops, 3 LLC refs  1µsec, 10 µJs
Online model recalibration
  Computation of least-square linear regression (16µsecs for ~30 samples)

## Slide 8: Request Power Accounting Results
Distribution of average request power
Distribution of request energy usage

## Slide 9: Validation of Request Power Accounting
Challenge of validation:
  Hard to know the ground truth – no way to directly measure request power or energy use on a multicore server
Validation approach #1:
  Aggregate accounted request energy over a time duration to estimate total system energy usage; then match with measurement
  No more than 9% error across six workloads on three machines
Validation approach #2:
  Use accounted request energy to estimate system energy usage at hypothetical workload conditions (different mixes/rates of requests)
  No more than 11% error for workloads with stable-behavior requests

## Slide 10: Fair Request Power Conditioning
Control max power use of a server machine
  Set equal per-request power budget for fairness
  Power containers track request power usage, throttle high-power requests using core duty-cycle modulation
A case study of Google App Engine with power viruses
  Keep max power at 40Watts
  Power containers: 33% slowdown for power viruses; 2% slowdown for normal requests
  Alternatively slow down all requests indiscriminately (13%) to lower the max power

## Slide 11: Heterogeneity-Aware Request Distribution
Different workloads/requests exhibit different levels of machine preferences in energy efficiency
  Energy usage on Intel SandyBridge over energy usage on Woodcrest
Power containers can capture fine-grained request energy profiles and distribute load in a server cluster for high efficiency
  Case study shows 25% energy saving compared to alternatives

## Slide 12: Conclusions
High-level messages:
  Fine-grained power accounting and control are important for multicore server efficiency and dependability
    Increasingly so on more power-proportional hardware and dynamic-behavior workloads (web 2.0, cloud computing, …)
  Possible to support these at the OS (on today’s processor hardware, requiring no application assistance)
New techniques:
  Enhanced modeling to account for multicore shared power
  Use online measurement to mitigate power model inaccuracy
  OS-level online request tracking and control